| EVENT: C2101 | DATE: | BRIEF TIME: |
| --- | --- | --- |
| INSTRUCTOR: | Aircraft: |
| BLOCK C21 | TITLE Cockpit Procedures | MEDIA CPT | Dual | Solo | Hrs 9.0 | H/X 1.5 |
|  |  |  | 6 | 0 |  |  |
| Syllabus Notes Practice all checklists, applicable FTI briefings, radio calls, and basic aircraft control. Ensure student’s checklist proficiency is adequate to proceed to flight operations. Multiple items are listed as discuss items. However, due to time constraints, it will not be possible to discuss all items prior to the simulator event. Therefore, a discuss item may be addressed during the sim and/or prior to the sim. During all C21xx events, each normal checklist should be performed if it has been previously introduced or discussed. C2101 and C2102, only normal checklists should be practiced. Due to the visual capability of the TC-12B simulator, all remaining C21XX events may include flight and visual maneuvers. For example, aborted takeoffs, SSE, basic air work, etc. Special Syllabus Requirements None Discuss Items Seat/rudder adjustment, fuel management panel, pilot instrument panel, engine instruments and switches, center instrument panel, annunciator panel/analysis, copilot instrument panel, circuit breaker panels, control pedestal, overhead control panel, brake check, checklists: before start, engine start, after start, engine run-up, takeoff, after landing and secure. a. See NATOPS and FTI Chapter 1 and Appendix E Emergency Procedures None Review Material Operating Condition Torque ft-lb Max ITT N1 Prop RPM Oil Press Oil Temp Start 1000 (5sec) -40 (min) Low Idle 660 52-55 60 (min) -40 to 99 High Idle 70-73 -40 to 99 Takeoff and Max Cont 2230 750 101.5 2000 105-135 10 to 99 Max Cruise/Climb 2230 725 101.5 2000 105-135 10 to 99 Max Reverse 750 88 1900 105-135 10 to 99 Transient 2750 (5sec) 850 (10sec) 102.6 (10sec) 2200 (5sec) 100 to 104 (5min) |