T-44A Briefing Guides

EVENT: C2101

DISCUSS ITEMS:  Seat/rudder pedal adjustment, fuel management panel, pilot instrument panel, engine instrument panel, engine instruments and switches, center instrument panel, annunciator panel/analysis, copilot instrument panel, circuit breaker panels, control pedestal, overhead control panel, checklists: before start, engine start, after start, brake check (out of chocks), engine runup, takeoff, after landing, and secure.

seat/rudder pedal adjustment – a two-position fore and aft adjustment of the pedals is provided through control levers on each pedal. The pilot compartment seats are adjustable fore and aft with the inboard handle on each pilot seat and vertically with the outboard handle. The three seat in the cabin area may be reclined but may not be moved fore and aft without maintenance support.

fuel management panel – cockpit  controls of the fuel system functions are directed from the fuel management panel. This panel contains the switches for the firewall shutoff valves, boost pumps, fuel transfer pumps, fuel transfer test, a switch for the crossfeed system, fuel system circuit breakers, fuel quantity indicators, and the fuel quantity selector switch.

pilot instrument panel –

engine instrument panel –

engine instruments and switches –

- Interstage Turbine Temperature Indicators – the ITT gauges are calibrated in degrees Celsius. Each gauge is connected to a thermal sensing element that is located in the hot gases between the turbine wheels. The ITT gauges register the temperature present between the compressor turbine and power turbine for the corresponding engine.

- Turbine Tachometers – The turbine tachometers register compressor turbine rpm (N1) for the respective engine. These indicators register as a percentage of maximum compressor turbine rpm. Each instrument is slaved to a tachometer generator attached to the respective engine mounted on the lower accessory section.

- Engine Torquemeters – Each engine torquemeter indicates torque applied to the propeller shaft of the corresponding engine. The torque applied to the propeller shaft generates an equal and opposite reaction on a movable ring gear located in the first reduction gear stage. Movement of the ring gear operates a variable oil metering orifice, metering engine oil pressure across the orifice to a calibrated pressure transmitter in proportion to torque sensed. The torque transmitter sends a 26-volt AC signal to the engine torque gauges that show torque in 100 foot-pound increments. The torquemeter circuits are protected by their respective circuit breaker, placarded torquemeter left and right, located on the engine instrument circuit breaker panel.

- Propeller Tachometers – The propeller tachometers register propeller speed in hundreds of rpm. Each indicator is slaved to a tachometer generator unit attached to the corresponding engine mounted on the reduction gear case 1 o’clock position.

- Fuel Flow Indicators – The fuel flow gauges register the rate of flow for consumed fuel via the fuel flow transmitters that are located between the fuel filter and oil to fuel heater in the fuel lines of the respective engines. Flow indicators receive electrical DC power from the No. 1 and No. 2 DC subpanel buses and are calibrated to show the flow of fuel in increments of hundreds of pounds per hour. Circuit protection is provided via the circuit breakers placarded FUEL FLOW and located on the copilot outboard circuit breaker panel.

- Oil Pressure and Oil Temperature Indicator – The combination oil pressure and oil temperature indicators are electrically powered by the No. 1 and No. 2 subpanel DC buses and indicate oil pressure in psi and oil temperature in degrees Celsius at the delivery side of the oil pump for each engine. Circuit protection of the oil temperature and pressure indication system is provided via the circuit breakers placarded OIL TEMP & PRESS and located on the copilot circuit breaker panel.

center instrument panel –

annunciator panel/analysis –

The annunciator panel mounted across the top of the instrument panel glareshield provides a visual monitor for critical functions of the aircraft and indicates conditions for which appropriate corrective action must be taken. Then panel presents two rows of small, rectangular windows that illuminate as either yellow, red, or green. Wordprinting on individual windows identifies the monitored functions, status, or fault condition. Active elements of the panel include a FAULT WARNING light, individual function status and fault lights, and DIM and PRESS TO TEST controls. A function indication is displayed by illumination of an appropriate yellow window. Fault indications are shown by illumination simultaneously of a specific red-colored window with flashing of the FAULT WARNING light. A status condition is indicated by illumination of an appropriate green window. The annunciator light system is powered by the No. 1 subpanel bus and is protected by a circuit breaker placarded ANN LIGHTS and located in the INDICATOR section of the copilot outboard subpanel.

copilot instrument panel –

circuit breaker panels –

Electrical bus locations of specific circuit breakers can be found in NATOPS pp. 2-23 and 2-24.

control pedestal –

overhead control panel –

before start checklist – Accomplish the Before Start Checklist in accordance with NATOPS and Appendix E of the FTI. NOTE: If a lineman is not standing by when ready to start, turn on the avionics master and contact “Peg Base” (138.775). A start brief shall be given. Instructors may accept a “standard” brief during subsequent evolutions with the same student.

engine start checklist – Start engines in accordance with NATIOS and Appendix E of the FTI. If starting during darkness, the CP should use a flashlight to provide extra illumination of the gauges (especially ITT). Panel lights may dim significantly when the starter is energized. NOTE: Should an APU start be required, see Section III of NATOPS.

after start checklist – Accomplish the After Start Checklist in accordance with NATOPS and Appendix E of the FTI.

brake check (out of chocks) – In order to free the lineman, hold the checklist after completing Step 5 (Avionics Master—ON) of the After Start Checklist. Brief the CP, then signal “brake check” to the lineman (the signal resembles one hand “talking”).  When signaled to move forward, report “Clear left.” CP responds “Clear right.” Taxi slowly forward as directed for a brake check and direct the CP to contact base (140.325) for a VHF radio check. A typical brief would be: “Keep the right side clear during all ground operations.” A typical radio call would be: “Montana Base, Montana ___ is out of the chocks.”

After the lineman is saluted and the aircraft stopped, set the parking brake and direct the CP to continue the checklist.

engine runup checklist – Accomplish the Engine Runup Checklist in accordance with NATOPS and Appendix E of the FTI. Taxi into the run-up area and stop with approximately 15’ wingtip distance between the next aircraft and yours. Ensure the nosewheel is not cocked and is aligned with runway heading. NOTE: The propeller of the outboard engine shall not cross the runway edge marking of RWY 4/22 while maneuvering the runup area. Doing so could result in a propeller striking a runway edge light.

takeoff checklist – Accomplish the Takeoff Checklist in accordance with NATOPS and Appendix E of the FTI. NOTES: (1) Block assignments/instrument departure requests shall be made from the runup area on all FAM/BI/FORM flights. If takeoff is not commenced within 30 minutes, cancel your block reservation with Seagull so the airspace may be utilized by other aircraft. (2) If a return to the field in VMC conditions is not possible, ensure an approach above minimums is available in the local area, and IAPs are readily accessible.

after landing checklist – the After Landing Checklist must be completed after each full stop landing (unless taxiing back on the active runway for immediate takeoff). The P should not call for or perform individual items of the After Landing Checklist until clear of the active runway.

To avoid a traffic jam on the taxiway, it is advisable to contact ground for taxi after clearing the active runway, and then call for the checklist as you taxi inbound. Ensure the PAC delegates appropriate checklist items to CP to allow full concentration on taxiing the aircraft safely.

secure checklist – Unless cockpit duties preclude it, P calls “First five items of the Secure Checklist” upon completion of the After Landing Checklist. The checklist may be held as required to request parking spot or to report arrival.