CDS

Pre Slowdown (LM)

Personnel seated forward of load

Checks CDS arming switches (245) are in normal position

Checks forward barrier (BSA for 5001 lbs loads or 10Klbs chains)

Checks ADS ramp support arms connected

Checks rigging (including retriever cable and knife)

Removes vertical restraint (if no CVR)

Red light - On

Don’s helmet & restraint harness

Slowdown

Open ramp and door (if doesn’t open from front, LM climbs over

loads to his control panel)

Checks static line retriever cable compression spring

Arms CDS switch (checks other in normal position)

Drop and Completion of Drop

“Green Light”

Static line retreiver rewinds for 3 seconds

Gates are cut by knife

LM sees gate cut then de-arms CDS switch

LM calls “Load Clear” or the condition

NOTE: If gate fails to cut, LM can manually cut if prebriefed.

Red Light - On, resets flaps to 50%

LM manually retrieves the static lines

LM clears Engineer to close ramp and door

No-Drop

LM Acknowledges

De-arms CDS switch

Clears closing of the ramp and door

Accomplished completion of drop checklist

NOTE: If drop reattempted, begin with pre slowdown checklist

EMERGENCY

Extend additional flaps and lower the nose

Maintain Drop airspeed and AGL

Avoid flying over or upwind of water or built up areas

Raise aft anchor cable (if required), Close ramp and door

Secure load

Completion of drop checklist