## Slide 1: .
ACP Battens enroute Stinson
800 MSL
90 KIAS
Straight and Level

## Slide 2: .
A/C yaws right
Climbing through 1000 MSL
Increase in engine noise

## Slide 3: .
.

## Slide 4: ENGINE OVERSPEED
1. Collective - increase
2. Throttle - reduce
3. Emer Gov Ops
  1. Gov Switch - Emer
  2. Throttle - adjust as necessary to control RPM
  3. Land as soon as possible

## Slide 5: WARNING
<footer>
<date/time>
Land even if manual throttle corrects the overspeed since there is a chance of an impending engine failure due to the debris generated by the initial N2 failure.

## Slide 6: CAUTION
<footer>
<date/time>
The maximum engine torque available for any ambient condition will be reduced by 6 to 8 PSI when the GOV AUTO/EMER switch is placed in the EMER position.

## Slide 7: FUEL CONTROL
<footer>
<date/time>
If the N2 Governor malfunctions, throttle reduction will result in a corresponding decrease in N2 RPM.
In the event of a fuel control malfunction, throttle reduction will have NO effect on N2 RPM.