## Slide 1: .
ACP Bridge en-route Stinson
800 MSL
90 KIAS
Straight and Level

## Slide 2: .
Sharp rumble
Severe engine vibration
Gages fluxing

## Slide 3: .
Erratic rumble
Erratic engine vibration
Erratic, fluxing gages
Decreased power available
EGT higher than normal

## Slide 4: ENGINE COMPRESSOR STALL
Collective - Reduce
De-Ice and Bleed Air Switches - OFF
Land as soon as possible

## Slide 5: CAUSES & CONSIDERATIONS
<footer>
<date/time>
Compressor blades exceeding the critical angle of attack
Dirt accumulation on compressor blades
Inlet guide vanes failed
Bleed bands failed
Incorrect fuel scheduling

## Slide 7: What are the EGT limits?
<footer>
<date/time>
Green: 400-610 continuous
Yellow: 610-625 for 30 minutes
Red: 625 maximum for 30 minutes
625-675 for 10 seconds (starting and acceleration)
675-760 for 5 seconds (starting and acceleration)
Red: 760 maximum