## Slide 1: EP OF THE DAY

## Slide 2: .
Input data here

## Slide 3: .
Abnormal feedback in cyclic and pedals are stiff.

## Slide 4: HYDRAULIC POWER FAILURE
1. Airspeed -- Adjust as necessary to attain the most comfortable level of control movements.
2. HYD CONT circuit breaker -- Out
If Hydraulic Power is not restored:
3. HYD CONT circuit breaker -- In
4. Land as soon as practical at an area that will permit a run-on landing with power. Maintain airspeed at or above ETL until touchdown.

## Slide 5: HYDRAULIC QUESTIONS
1. What is the normal operating PSI of system?
800 PSI
2. When will the HYD PRESSURE light illuminate?
500 +- 100 PSI
3. When will it extinguish?
800 +- 100 PSI
4. How much pressure is trapped in the irreversible valves when the hydraulic power fails?
500 PSI