## Slide 1: Emergency Procedure Review
Main driveshaft failure
Total engine malfunction in-flight
Engine underspeed
Engine overspeed
IGV closed position
N2 spur gear
Compressor stall

## Slide 2: .
ACP Battens enroute Lucas
800 MSL
90 KIAS
Straight and Level

## Slide 3: .
Loud noise
Severe left yaw
Increase in engine noise
Some vibrations
A/C descending @ 1000 ft/min
Passing 700’ MSL

## Slide 4: .
VVI 2000 ft/min
A/C passing 600 MSL
Increased engine noise
Still have vibrations

## Slide 5: .
A/C passing 500’ MSL
VVI 1800 ft/min
Increased engine noise
Still have vibrations

## Slide 6: .
A/C passing 400’ MSL
VVI 2000 ft/min
Decreasing engine noise
Vibrations subsiding

## Slide 7: MAIN DRIVESHAFT FAILURE
<date/time>
1. Autorotate
  Collective - Adjust
  Pedals - Adjust
  Throttle - Adjust
  Airspeed - Adjust
2. Emergency Shutdown
  Throttle - Off
  Fuel Switches - Off
  Bat switch - OFF

## Slide 8: When does the RPM Warning Light Illuminate?
<footer>
<date/time>
NR 329-339 (high warning)
NR 300-310 (low warning)
N2 6100-6300 (low warning)
Loss of signal from either NR or N2 tach generator

## Slide 9: When does the Horn and RPM Warning Light Illuminate?
<footer>
<date/time>
NR 330-310 (low warning) with N2 6100-6300 (low warning)
Loss of signal from BOTH NR or N2 tach generator

## Slide 10
<footer>
<date/time>

## Slide 11
<footer>
<date/time>

## Slide 12: Engine Malfunction
<footer>
<date/time>
Autorotate
Emer Gov Ops
Engine restart during flight (if able)

## Slide 13: .
4NM northwest of RT-563 in friendly territory.
200’ AGL 90 KIAS

## Slide 14: .
Left yaw

## Slide 15: .
.

## Slide 16: Engine Malfunction
<footer>
<date/time>
Autorotate
Emer Gov Ops

## Slide 17: EMERGENCY GOV OPERATION
Gov Switch -- EMER
Throttle -- Adjust as necessary to control RPM
Land as soon as possible

## Slide 18: CONSIDERATIONS
Maximum engine torque will be reduced by how much when Gov Switch is in EMER?
6-8 PSI

## Slide 24: .
Enroute to RT Bonnie (NW of Florala)
Currently 2 NM east of RT Linda
Currently 200’ AGL

## Slide 25: .
A/C yaws right
Climbing through 400’ AGL
Increase in engine noise

## Slide 26: .
Climbing through 600’ AGL
Increase in engine noise

## Slide 27: .
Currently at 800’ AGL
½ NM south of RT Linda
Winds 180/20

## Slide 28: ENGINE OVERSPEED
<footer>
<date/time>
1. Collective - increase
2. Throttle - reduce
3. Emer Gov Ops
  1. Gov Switch - Emer
  2. Throttle - adjust as necessary to control RPM
  3. Land as soon as possible

## Slide 29: WARNING
<footer>
<date/time>
Land even if manual throttle corrects the overspeed since there is a chance of an impending engine failure due to the debris generated by the initial N2 failure.

## Slide 30: CAUTION
<footer>
<date/time>
The maximum engine torque available for any ambient condition will be reduced by 6 to 8 PSI when the GOV AUTO/EMER switch is placed in the EMER position.

## Slide 31: FUEL CONTROL
<footer>
<date/time>
If the N2 Governor malfunctions, throttle reduction will result in a corresponding decrease in N2 RPM.
In the event of a fuel control malfunction, throttle reduction will have NO effect on N2 RPM.

## Slide 32: .
Climbing right turn from Golf Pad @ Lowe enroute to SWC
Passing 600 MSL
A/S 70 KIAS

## Slide 33: .
A/C ceased its climb, and is beginning to descend

## Slide 34: .
Level flight @ 70 KIAS

## Slide 35: INLET GUIDE VANE FAILURE (Closed Position)
<footer>
<date/time>
A maximum of 20-25 PSI of torque is available although N1 may appear normal.
Power applications above 20-25 will result in the deterioration of NR and N2 while increasing the N1 and EGT.
Accomplish an approach and landing to the ground with torque not exceeding the maximum available. If possible, a running landing is recommended.

## Slide 36: INLET GUIDE VANE FAILURE (Open Position)
<footer>
<date/time>
If this occurs during normal flight, it is likely no indications will be evidenced.
Increased acceleration times will be experienced.
As power applications are made from increasingly lower N1 settings, acceleration times will correspondingly increase.

## Slide 37: What is the purpose of the IGV’s
<footer>
<date/time>
To change the angle of attack between the inlet air and first compressor rotor blades.
Maintain airflow requirements of the compressor rotor assembly which provides additional surge margins.
Operated and controlled by the Fuel Control Unit (fuel pressure actuated)
Closed at low RPM / Open at high RPM

## Slide 39: What are the differences between Inlet Guide Vane Failure and a Droop Compensator Failure?
<footer>
<date/time>

## Slide 40: .
5 NM west of RT 563-Linda
1000 MSL
90 KIAS
Straight and level

## Slide 41: .

## Slide 42: .

## Slide 43: .

## Slide 44: N2 Spur Gear Failure
1. Collective -- Increase
2. Throttle -- Reduce until normal operating RPM is attained
3. Land as soon as possible

## Slide 45: N2 Gearbox

## Slide 46: .
ACP Battens enroute Lucas
800 MSL
90 KIAS
Straight and Level

## Slide 47: .
Sharp rumble
Severe engine vibration
Guages fluxing

## Slide 48: .
Occasional rumble
Occasional engine vibration
Occasional guages fluxing
A/C descending @ 200 ft/min

## Slide 49: ENGINE COMPRESSOR STALL
<footer>
<date/time>
Collective - Reduce
De-Ice and Bleed Air Switches - OFF
Land as soon as possible

## Slide 50: CAUSES & CONSIDERATIONS
<footer>
<date/time>
Exceeding the critical angle of attack of compressor blades.
Dirt accumulation on compressor blades.
Inlet guide vanes may fail.
Bleed band may fail by not preventing back flow.
Fuel scheduling may be higher than normal.

## Slide 52: What are the EGT limits?
<footer>
<date/time>
Green: 400-610 continuous
Yellow: 610-625 for 30 minutes
Red: 625 maximum for 30 minutes
625-675 for 10 seconds (starting and acceleration)
675-760 for 5 seconds (starting and acceleration)
Red: 760 maximum