## Slide 1: Settling with power
A flight condition when collective inputs are ineffective in arresting a rate of descent due to an unsteady airflow about the rotor system
Helicopter settles in its own downwash

## Slide 2: Contributory Conditions
Vertical or near vertical descent
Rotor system using all or some of the avail engine power.
Loss of ETL

## Slide 3: Corrective Actions
Reduce sink rate early on, or
Increasing airspeed and lowering collective pitch

## Slide 4: Corrective Actions
Reduce sink rate early on, or
Increasing airspeed and lowering collective pitch

## Slide 5: Corrective Actions
Maintain a stable controlled approach, or
Better have a good escape option

## Slide 6: Corrective Actions
Maintain a stable controlled approach
Go around early in the approach, or
Better have a good escape option