## Slide 1: .
ACP Battens enroute Lucas
800 MSL
90 KIAS
Straight and Level

## Slide 2: .
Loud noise
Severe left yaw
Increase in engine noise
Some vibrations
A/C descending @ 1000 ft/min
Passing 700’ MSL

## Slide 3: .
VVI 2000 ft/min
A/C passing 600 MSL
Increased engine noise
Still have vibrations

## Slide 4: .
A/C passing 500’ MSL
VVI 1800 ft/min
Increased engine noise
Still have vibrations

## Slide 5: .
A/C passing 400’ MSL
VVI 2000 ft/min
Decreasing engine noise
Vibrations subsiding

## Slide 6: MAIN DRIVESHAFT FAILURE
1. Autorotate
  Collective - Adjust
  Pedals - Adjust
  Throttle - Adjust
  Airspeed - Adjust
2. Emergency Shutdown
  Throttle - Off
  Fuel Switches - Off
  Bat switch - OFF

## Slide 7: When does the RPM Warning Light Illuminate?
<footer>
<date/time>
NR 329-339 (high warning)
NR 300-310 (low warning)
N2 6100-6300 (low warning)
Loss of signal from either NR tach generator
or
N2 tach generator

## Slide 8: When does the Horn and RPM Warning Light Illuminate?
<footer>
<date/time>
NR 300-310 (low warning) with N2 6100-6300 (low warning)
Loss of signal from BOTH
NR and N2 tach generators