## Slide 1: NVG Academics
23 FTS

## Slide 2: Overview
Fundamentals of Night Vision
Anatomy of the Eye
Monocular Cues
Visual Illusions
Hemispherical Illumination and Meteorological Conditions
Night Operations

## Slide 3: Fundamentals of Night Vision
Types of Vision
  Photopic
  Mesopic
  Scotopic
Day versus Night Vision
Notes: PHOTOPIC: Day type vision, uses cones cells concentrated in the fovea
centralis. Sharp image and color vision .
MESOPIC: Dawn or dusk and or full moon. Vision uses both rods and cones,
crew members should use off center vision.
SCOTOPIC: Low light levels, rod cells become more effective, poor detail,
acuity less than 20/200, loss of color vision, and night blind spot
now present in central field.

## Slide 4: Anatomy of the Eye
Rods
Cones
Night Blind Spot
Day Blind Spot

## Slide 5: Anatomy of the Eye

## Slide 6: Night Blind Spot

## Slide 7: Visual Problems
Hyperopia
Night Myopia
Astigmatism
Presbyopia
Miosis

## Slide 8
Hyperopia

## Slide 9
Myopia

## Slide 10
Astigmatism
Notes: ASTIGMATION: Irregularity of the shape of the cornea or lens resulting in the inability to focus on different meridians simultaneously.(poles and wires)

## Slide 11: Monocular Cues
Geometric Perspective
  Linear Perspective
  Apparent Foreshortening
  Vertical Positioning in the Field
Retinal Image Size
  Known Size of Objects
  Increasing/Decreasing Size of Objects
  Terrestrial Association
  Overlapping Contours
Notes: 1-11. DISTANCE ESTIMATION AND DEPTH PERCEPTION
Distance estimation and depth perception cues are easily recognized when crewmembers use central vision under good illumination. As the light level decreases, the ability to judge distances accurately is degraded and visual illusions become more common. A knowledge of distance estimation and depth perception mechanisms and cues will assist crew members in judging distances at night. These cues may be monocular or binocular. Monocular cues are more important for crewmembers than binocular cues.
a. Monocular Cues. The monocular cues that aid in distance estimation and depth perception include motion parallax, geometric perspective, retinal image size, and aerial perspective.

## Slide 12: Geometric Perspective
Notes: (2) Geometric perspective. An object may appear to have a different shape when viewed at varying distances and from different angles. Geometric perspective cues include linear perspective, apparent foreshortening, and vertical position in the field. They are illustrated in Figure 1-9. -
(a) Linear perspective. Parallel lines, such as runway lights, tend to converge as distance from the observer increases. This is illustrated in part A of Figure 1-9.
(b) Apparent foreshortening. The true shape of an object or a terrain feature appears elliptical when viewed from a distance. As the distance to the object or the terrain feature decreases, the apparent perspective changes to its true shape or form. Part B of Figure 1-9 illustrates how the shape of a body of water changes when viewed at different distances at the same altitude.
(c) Vertical position in the field. Objects or terrain features farther away from the observer appear higher on the horizon than those closer to the observer. The higher vehicle in part C of Figure 1-9 appears to be closer to the top and, thus, at the greater distance from the observer. At night, crew members can mistake lights on elevated structures or lights

## Slide 13
Known Size of Objects

## Slide 14: Terrestrial Association
Notes: (c) Terrestrial associations. Comparing an object, such as an airfield, with an object of known size, such as a helicopter, helps to determine the object's size and apparent distance from the observer objects ordinarily associated together are judged to be at about the same distance

## Slide 15: Overlapping Contours
Notes: (d) Overlapping contours or interposition of objects. When objects overlap, the overlapped object is farther away, as illustrated in Figure 1-12. This overlapping is especially important to consider at night during a landing approach. Lights disappearing or flickering in the landing area indicate barriers between the landing area and the aircraft. The flight path should be adjusted accordingly.

## Slide 16: Monocular Cues (Continued)
Aerial Perspective
  Variations in Color or Shade
  Loss of Texture or Detail
  Position of Light Source and Direction of Shadow
Motion Parallax
Notes: (4) Aerial perspective. The clarity of an object and the shadow cast by it are perceived by the brain and are cues for estimating distance. Several aerial perspective factors are used to determine distance.
(a) Variations in color or shade. Subtle variations in color or shade are clearer the closer the observer is to an object. However, as distance increases, these distinctions blur. For example, the side of a hill from a distance will appear to be a uniform shade with no distinguishable shape. As the aircrew flies closer to the hill, the shades produced by individual trees and the spaces in between those trees become noticeable. Thus under high light levels at night, color or shade can provide cues for distance estimation.
(b) Loss of detail or texture. As a person gets farther from an object, discrete details become less apparent. For example, when a cornfield becomes a solid color and the leaves and branches of a tree become a solid mass, the objects are judged to be far away. Because reduced illumination also decreases resolution, these cues will disappear shortly after sunset or be limited to close viewing distances.
(c) Position of light source and direction of shadow. Every object will cast a shadow from a light source. The direction in which the shadow is cast depends on the position of the light source. If the shadow of an object is toward the observer, the object is closer than the light source is to the observer. Figure 1-13 illustrates light and shadows. For example, a helicopter observed near an airport is judged to be in the traffic pattern and, therefore, at about the same distance as the airfield. Figure 1-11 illustrates terrestrial association.
(1) Motion parallax. This cue to depth perception is a means of judging distances under reduced illumination. Motion parallax refers to the apparent motion of stationary objects as viewed by an observer moving across the landscape. When the crewmember looks outside the aircraft, perpendicular to the direction of travel, near objects appear to move backward, past, or opposite the path of motion. Far objects seem to move in the direction of motion or remain fixed. The rate of apparent movement depends on the distance the observer is from the object. For example, as an aviator flies low level, objects near the aircraft will appear to rush past the aircraft while a mountain range near the horizon will appear stationary. As the aviator flies across a power line that extends to the horizon, that part of the power line near the aircraft will appear to move swiftly, opposite the path of motion. Toward the horizon, the same power line will appear fixed.

## Slide 17: Visual Illusions (Continued)
AUTOKINESIS
GROUND LIGHT MISINTERPRETATION
RELATIVE MOTION
REVERSIBLE PERSPECTIVE
FALSE HORIZONS
Notes: 1-12. VISUAL ILLUSIONS
Decreasing visual information increases the probability of spatial disorientation. Reduced visual references also create several illusions that can induce spatial disorientation. Many types of visual illusions can occur in the aviation environment. Included among them are autokinesis, ground light misinterpretation, relative motion, reversible perspective illusion, false horizons, altered reference planes, and height perception illusion, others include flicker vertigo, fascination (fixation), structural illusions, and size-distance illusion.
a. Autokinesis. When a static light is stared at in the dark, the light appears to move, as shown in Figure 1-14. This phenomenon can be readily demonstrated by staring at a lighted cigarette in a dark room. Apparent movement will begin in about 8 to l0 seconds. Although the cause of autokinesis is not known, it appears to be related to the loss of surrounding references that normally serve to stabilize visual perceptions. This illusion can be eliminated or reduced by visual scanning, by increasing the number of lights, or by varying the light intensity. The most important of the three solutions is visual scanning. A light or lights should not be stared at for more than 10 seconds. This illusion is not limited to light in darkness. It can occur whenever a small, bright, still object is stared at against a dull dark or nondescript background. Similarly, it can occur when a small, dark, still object is viewed against a light, structureless environment. Anytime visual references are not available, aircrews are subject to this illusion.
b. Ground Light Misinterpretation. A common occurrence is to confuse ground lights with stars. When this happens, aviators unknowingly position aircraft in unusual attitudes to keep the ground lights--believed to be stars--above them. For example, some aviators have mistaken the lights along a seashore for the horizon and have maneuvered their aircraft dangerously close to the sea; they believed they were flying straight and level. Aviators have also confused certain geometric patterns of ground lights. For example, aviators have identified moving trains as landing zone lights and have been badly shaken by their near misses. To avoid these problems, aviators should cross-check aircraft instruments. Also, position lights of other aircraft in formation can be mistaken for ground lights and might be lost against the horizon when another aircraft is at or below the altitude of the observer. Figure 1-15 illustrates ground light and skylight illusion.
c. Relative Motion. The illusion of relative motion can be illustrated by an example. An aviator hovers an aircraft and waits for hover taxi instructions. Another aircraft hovers alongside. As the other aircraft is picked up in the first aviator's peripheral vision, the aviator senses movement in the opposite direction. This illusion may be encountered during multi-helicopter operations. Aircrews may mistake the motion of another aircraft for that of their own. The only way to correct for this illusion is to have sufficient experience to understand that such illusions do occur and to not react to them on the controls. The use of proper scanning techniques can help prevent this illusion.
d. Reversible Perspective Illusion. At night, an aircraft may appear to be going away when it is, in fact, approaching a second aircraft. This illusion often occurs when an aircraft is flying parallel to another's course. To determine the direction of flight, aircrews should observe aircraft lights and their relative position to the horizon. If the intensity of the lights increases, the aircraft is approaching. If the lights dim, the aircraft is moving away. Also, remembering the '13 Rs" will help identify the direction of travel when other aircraft are encountered. If the red aircraft position lights are on the right, the aircraft is returning (coming toward the observer).
e. False Horizons. Cloud formations may be confused with the horizon or the ground. Momentary confusion may result when the aviator looks up after having given prolonged attention to a task in the cockpit. Because outside references for attitude are less obvious and reliable at night, aviators should rely less on them during night flight. Using instrument cross-checks can help prevent this situation. While hovering over terrain that is not perfectly level, aviators might mistake the sloped ground in front of the aircraft for the horizon and cause the aircraft to drift while trying to maintain a stationary position. Figure 1-16 illustrates false horizon illusion.

## Slide 18: Visual Illusions
ALTERED PLANES
HEIGHT PERCEPTION
FLICKER VERTIGO
FASCINATION/FIXATION
STRCUTURAL ILLUSIONS
SIZE DISTANCE ILLUSION
Notes: f. Altered Reference Planes. When approaching a line of mountains or clouds, aviators may feel that they need to climb even though their altitude is adequate. Also, when flying parallel to a line of clouds, aviators may tend to tilt the aircraft away from the clouds.
g- Height Perception Illusion. When flying over desert, snow, water, or other areas of poor contrast, crew members may experience the illusion of being higher above the terrain than they actually are. This is due to the lack of visual references. This illusion may be overcome by dropping an object, such as a chemical light stick or flare, on the ground before landing. Another technique to overcome this illusion is to monitor the shadows cast by near objects, such as the landing gear, or skid shadows at a hover. Flight in an area where visibility is restricted by haze, smoke, or fog produces the same illusion.
h. Flicker Vertigo. Much time and research have been devoted to the study of flicker vertigo. A light flickering at a rate between 4 and 20 cycles per second can produce unpleasant and dangerous reactions. Such conditions as nausea, vomiting, and vertigo may occur. On rare occasions, convulsions and unconsciousness may also occur. Fatigue, frustration, and boredom tend to intensify these reactions. During the day, the problem can be caused by sunlight flickering through rotor blades or propellers. At night, it can also be caused by an anticollision light reflecting against an overcast sky, haze, or the rotor system. This can be corrected by turning the anticollision light off.
    i. Fascination (Fixation). This illusion occurs when aviators ignore orientation cues and fix their attention on a goal or an object. This is dangerous because aircraft ground-closure rates are difficult to determine at night; normal daylight peripheral movement is reduced or absent. Target hypnosis is a common type of fascination. For example, an aviator intent on hitting a target during a gunnery run may delay pull-up so long that the aircraft contacts the ground. Preventing this illusion requires increased scanning by the aviator.
    j. Structural Illusions. Structural illusions are caused by heat waves, rain, snow, sleet, or other factors that obscure vision. For example, a straight line may appear to be curved when seen through a desert heat wave or a wing-tip light may appear to double or move when viewed during a rain shower.
k. Size-Distance Illusion. This illusion results from viewing a source of light that is increasing or decreasing in luminance (brightness). The aviator may interpret the light as approaching or retreating. For example, when an aviator, hovering near a second aircraft, changes the position lights from DIM to BRIGHT, the other aircraft may appear to jump toward him.

## Slide 19: False Horizons

## Slide 20: Hemispherical Illumination
Lunar Light
  Moon Phases
    New Moon
    First Quarter
    Full Moon
    Third (Last) Quarter
Solar Light
Artificial Light
Notes: Each moon phase takes about seven days. Moon angle changes 15
degrees per hour.
Solar light becomes unusable 12 degrees below the horizon

## Slide 21: Hemispherical Illumination
Meteorological Effects
  Clouds
  Fog, Dust, Haze, Smoke
  Lightning
Notes:     A. Clouds -
  (1) Clouds reduce hemispherical illumination to some extent. The exact amount of reflection or absorption of light energy by different cloud types is not known. Therefore, a common factor cannot be applied to each condition of cloud coverage. A subjective evaluation of light reduction caused by clouds can be made by considering the amount of cloud coverage and the density, or thickness, of the clouds. For example, a thick, overcast layer of clouds will reduce the ambient light to a much greater degree than a thin, broken layer of clouds. The combined effects of two or more layers of clouds must also be considered.
(2) Because of reduced night vision (unaided or aided), aviators may fail to detect a gradual increase in cloud coverage and may, without warning, inadvertently enter the clouds. At night aircrews must be alert for indications that clouds are present. Some of these indications are discussed below.
(a) The light level is gradually reduced. Visual acuity and terrain contrast are also reduced or lost.
(b) The moon and stars are obscured. The less visible the moon and stars,, the heavier the cloud coverage.
(c) Shadows obscure the moon's illumination. Crewmembers can detect these shadows by observing the varying levels of ambient light along the flight route.
B. Fog, Dust, Haze, and Smoke.
(1) Visibility restrictions reduce hemispherical illumination. Conditions such as ground fog, dust, haze, or smoke are more pronounced lower altitudes. Haze is common around large cities.
(2) The probability of fog increases as the temperature decreases and the dew point spread approaches zero. A decrease in the intensity of ground lights indicates an increase in the moisture content of the air. A halo effect around ground lights indicates that moisture is in the air and that ground fog may be forming. The halo effect is more pronounced with I' devices. Aviators using I' devices can "see" through fog, snow, and rain better than with the unaided eye. This may result in less reaction time for the aviator to avoid entering IMC.
C. Lightning. At least one meteorological phenomenon increases illumination. Lightning flashes have an effect similar to that of a bright flare. The intensity of the illumination depends on how near the lightning is. Night vision may be impaired if the aircrew is too close to lightning activity.

## Slide 22: Night Operations
Terrain Flight Modes
Physiological and Psychological Stressors
Environment
Maps and Visual Aids
Threat
Safety
Notes: TERRAIN FLIGHT: Depends on factors of METT-T ( mission ,enemy,terrain time and troops)
P/P STRESSORS:IP DEATH ( illness,physical condition, drugs, exhaustion, alcohol, tobacco, and hypoglycemia.)
ENVIRONMENT:Terrain interpretation will be affected by the seasons, flight altitude, and the familiarity of the man made in the A/O
MAPS AND VISUAL AIDS: Most commonly used maps are 1:250,000 ‘ 1:500,000, and 1:50,000. Visual aids such as aerial photos and sand tables/terrain should be uses whenever possible.
Threat:Current enemy situation, antiaircraft and ADA capability,and enemy’s surveillance capability.
SAFETY: The air mission commander must make a risk assessment while planning the mission, and continue to update the assessment during the mission so as to minimize the risk whenever possible.

## Slide 23: Conclusion
Fundamentals of Night Vision
Anatomy of the Eye
Monocular Cues
Visual Illusions
Hemispherical Illumination and Meteorological Conditions
Night Operations