# Text boxes

Random Steep

200 KIAS = 3 NMs (No Wind)

250 KIAS = 4.5 – 5.0 NMs (No Wind)

Start slowing 1 NM

from approach end

Start base turn when

even with landing

threshold (No Wind)

Success = 150 KIAS,

flaps 50%, gear in transit prior to base turn

Pull power over the runway and use  G’s to bleed airspeed when turning downwind

Use runway length to help judge offset

Success =

150 KIAS,

flaps 50%, gear in transit prior to base turn

Beam Approach

Straight-In Approach

Teardrop Approach