HE

Pre Slowdown (LM)

Personnel seated forward of load

Checks CDS arming switches (245) are in normal position

Removes emergency restraint on loads to be extracted

Checks right hand locks to ensure proper setting

Checks ADS ramp support arms connected

Inspects loads and extraction sysytem for proper rigging

Unlocks left hand locks for loads to be dropped

Red light - On

Don’s helmet & restraint harness

Slowdown

Open ramp and door (if doesn’t open from front, LM climbs over

loads to his control panel)

Engineer ensures ramp and door open light is illuminated for entire drop

(no light means no drop)

NOTE:  For the ADS to work, the aircraft must be airborne, ADS ramp

support arms connected, and ramp and door opened to the airdrop position

Drop and Completion of Drop

“Green Light” Co-pilot turns on green light and presses ADS button

Extraction chute is released and swings aft into airstream

NOTE: LM is positioned by T-handle to pull when he hears and sees green

light if extraction chute didn’t release

NOTE: LM standing by to pull right hand release handle (emergency position)

if load fails to extract with extraction chute out

LM calls “Load Clear” or the condition

Red Light - On

LM clears Engineer to close ramp and door

No-Drop

LM Acknowledges

Clears closing of the ramp and door

Restrains load

Accomplished completion of drop checklist

NOTE: If drop reattempted, begin with pre slowdown checklist

HE

EMERGENCY

Maintain Drop airspeed and AGL

Avoid flying over or upwind of water or built up areas

LM runs malfunction checklist and tells pilot when complete

If right hand locks release prior to green light

Apply emergency restraint (from front to rear)

Raise aft anchor cable support (if required)

Close ramp and door

Relock platforms (if unable, secure with aircraft tiedowns)

If extraction chute fails to release mechanically, or falls on the ramp

Apply emergency aft restraint (from front to rear)

Raise aft anchor cable support (if required)

Close ramp and door

Relock platforms (if unable, secure with aircraft tiedowns)

If load fails to extract with single extraction chute outside the aircraft

Apply emergency aft restraint (from front to rear)

Cut extraction line aft of the attachment point (forward-deploys chutes)

Raise aft anchor cable support (if required)

Close ramp and door

Relock platforms (if unable, secure with aircraft tiedowns)

If load fails to extract with multiple 28-foot outside the aircraft

Pull right rail control handle to emergency

If fails to extract, pull simul handle full forward (ensures left locks are out)

NOTE: Pull for 10-20 seconds to compensate for lock loading/binding

If still fails to extract, land. Forced landing likely.