PERSONNEL

Pre Slowdown (LM)

Red Light - On

Aux hydralic pump on for tailgate drops (co-pilot)

Alert Jumpmaster

CDS arming switches (245) in normal position

Troopers hook up and jumpmaster puts chute on (prior to opening door)

ADS arms connected (tailgate), attaches anchor cable to A frame (door)

Don’s restraint harness & helmet

Slowdown

Paratroop door drop

Flaps - 50% , co-pilot opens air deflector door

LM opens doors, visually checks for open air deflector doors

Jump platfroms locked in place, Jumpmaster assumes control of the exit

Tailgate drop

Ramp and door opened by engineer

Aft anchor arms lowered

Jumpmaster assumes control of the exit

Drop and Completion of Drop

LM alerts personnel of 1-minute and 5 seconds, Green Light - On

LM calls “Load Clear” or the condition (visually checks outside)

Red Light - On (LM regains control of exit)

Jump platform in,  static lines retreived, chutes dearmed, doors closed

+ Raise aft anchor cables supports, clear ramp & door for closing

No-Drop

LM Acknowledges, accomplishes completion of drop checklist

NOTE: If drop reattempted, begin with pre slowdown checklist

EMERGENCY (towed parachutist)

LM notifies Jumpmaster, Pilot

Red Light - On

Maintain drop airspeed and minimum AGL for chute used

Avoid flying over or upwind of water or built up areas

Jumpmaster/Loadmaster makes recommendation to pilot

Paratroop doors

Lower landing gear, 100% flaps (WRNG: ( aircraft performance)

Avoid turning into the towed jumper

Turns should be shallow and coordinated

First priority is to retrieve

Ramp and Door

First priority is to cut if concious

Rest flaps to 50% & raise landing gear

Completion of drop checklist

NOTE: conciousness indicated with tight body position/hand on reserve